## Slide 1: SEARCH – a New Slow Start Algorithm for TCP and QUIC
Jae Chung
Feng Li
Maryam Ataei Kachooei
Mark Claypool
IETF CCWG
Bangkok, Thailand
March 2025
UPDATE

## Slide 2
Congestion window doubles each RTT
Packet loss Exit slow start: Too late (After loss)
Idea: Exit after reaching capacity and before loss
HyStart (Linux default)
HyStart over wireless Too early (Before capacity)
Congestion Window
Time
Packet loss
Slow Start
Congestion Avoidance
TCP Slow Start
Capacity
Goal: At chokepoint: after capacity, before loss

## Slide 3
t1
t2
t3
t4
difference
Round-trip time
0
t5
threshold
SEARCH Concept

## Slide 4
t1
t2
t3
t4
t5
t6
delivered bytes
round-trip time
a
2a
4a
8a
diff = 2 prev_delv – curr delv
normalized diff = diff / (2 prev_delv )
if (normalized diff threshold):
exit from slow start
curr_delv
capacity
prev_delv
SEARCH Algorithm

## Slide 5: Outline
Introduction (done)
Place SEARCH in slow start space (next)
  Delay-based: HyStart, HyStart++
  Delivered Bytes-based: BBR, SEARCH
Memory use delivered byte history
Test framework
Summary

## Slide 6: Cubic (without HyStart)

## Slide 7: Delay-Based: HyStart
RTT “spikes”  exit SS
Sensitive to RTT variation  premature exit, underutilization
  Bad in high BDP networks

## Slide 8: Delay-Based: HyStart++
CA
CSS
CSS
While in CSS grow at slower rate than 2x
If HyStart was “wrong” – grow slower for some time
If HyStart was “right” – CSS pushes past capacity limit
Recognizes that delay increase a “noisy” signal
  Doesn’t have better signal!
Conservative Slow Start (CSS)
  Slower growth
  Check delay
Delay goes down?
  Yes  back to SS
  No  go to CA

## Slide 9: Delivered Bytes-Based: BBR
Exits when delivery rate stops growing
  3 consecutive rounds (RTTs), less than 25%
  Decision each round
When at capacity, RTTs increase  rounds increase

## Slide 10: Delivered Bytes-Based: SEARCH
Exits when delivered bytes increase less than 30% from previous RTT
Decision each bin boundary (about ½ RTT)
Uses initial RTT, not current  resilient to congestion delay

## Slide 11: 4G LTE – Same old story

## Slide 12: 4G LTE
BBR
SEARCH
HyStart
HyStart

## Slide 13: Outline
Place SEARCH in slow start space (done)
  Delay-based: HyStart, HyStart++
  Delivered Bytes-based: BBR, SEARCH
Memory use delivered byte history (next)
Test framework
Summary

## Slide 14: Memory Use for Delivered Bytes
BBR
  Time when every segment sent
  When segment delivered, compute delivery rate
    bytes delivered from sent to now / time
  Storage overhead – time size x cwnd size
SEARCH
  Sequence number each bin (~½ RTT)
  When bin ends, compute delivered
    seq now – seq then
  Storage overhead – sequence x window
Window 10 + History 15
= 25 total
100 Mb/s, 100 ms RTT
= 83 total
t0
t1
t2
-.
tN
s0
s1
..
sN

## Slide 15: Outline
Place SEARCH in slow start space (done)
  Delay-based: HyStart, HyStart++
  Delivered Bytes-based: BBR, SEARCH
Memory use delivered byte history (done)
Test framework (next)
Summary

## Slide 16
Source Code
Code Extraction
tcp.h
search_mod.c
search_defs.h
Setup Support Files
test_search.c
cc_helper_func.h
Compilation & Execution
Input csv
Output file
Kernel code
(tcp_cubic_search.c)
// SEARCH_defs_begin
// SEARCH_defs_end
// SEARCH_begin
// SEARCH_end
Server
Client
Input
CSV file
t1 s1
t2 s2
…
tn sn
Output
Log file
Pass
Pass
Fail
Pass
Challenges:
Verify implementations of SEARCH
Compare performance for parameter tuning

## Slide 17: Using the Framework
Verify and validate SEARCH implementations
  Linux, versions
  FreeBSD
  QUIC
Compare performance
  Traditional, HyStart, SEARCH
  BBR, HyStart++
Traces!
  Normal, edge cases
  WiFi, 4g/5g, GEO, LEO, Wired
Output
Log file
Pass
Pass
Fail
Pass

## Slide 18: Summary
SEARCH
  Determines “choke point” from expected delivered bytes
  Exits slow start after congestion point, before loss
Framework to verify implementations
Looking for volunteers to try SEARCH!
https://search-ss.wpi.edu/
claypool@wpi.edu

## Slide 19: SEARCH – a New Slow Start Algorithm for TCP and QUIC
Jae Chung
Feng Li
Maryam Ataei Kachooei
Mark Claypool
IETF CCWG
Bangkok, Thailand
March 2025
Thank-you for your attention!

## Slide 20: References
Improving TCP Slow Start Performance in Wireless Networks with SEARCH
  IEEE World of Wireless, Mobile and Multimedia Networks (WoWMoM)
  Perth, Australia, June 2024
Improving QUIC Slow Start Behavior in Wireless Networks with SEARCH
  IEEE Local and Metropolitan Area Networks (LANMAN)
  Boston, Massachusetts, USA, July 2024
Implementation of the SEARCH Slow Start Algorithm in the Linux Kernel
  0x18 NetDev Conference
  Santa Clara, California, USA, July 2024
Reducing Per-flow Memory Use in TCP SEARCH
  IEEE World of Wireless, Mobile and Multimedia Networks (WoWMoM)
  Fort Worth, TX, USA, May 2025

## Slide 21: TCP Congestion Control Test Framework
ss_extract.py - Extracts Relevant Code
  Usage: ss_extract.py -f original_file.c -k keyword
  Functionality:
    Extracts slow start-related code using labeled sections (keyword_begin, keyword_end, keyword_defs.begin, keyword_defs.end).
    Generates three key files in test_dir:
      keyword_modules.c
      keyword_defs.h
      tcp.h (based on extracted modules)

## Slide 22: TCP Congestion Control Test Framework
2. ss_setup.py - Sets Up Testing Environment
  Usage: ss_setup.py -k keyword
  Functionality:
    Determines the appropriate test file for the specified protocol.
    If a predefined test_keyword.c exists for the keyword (e.g., SEARCH, HyStart, BBR), it is placed in test_dir.
    If no predefined test file is available, test_base.c is provided for user modification.
    Places cc_helper_functions.h, which includes essential congestion control functions, in test_dir. Users can extend this file by extracting additional functions from the kernel if needed.

## Slide 23: TCP Congestion Control Test Framework
3. ss_run.py - Executes the Tests
  Usage: ss_run.py -k keyword -i input -o output
  Functionality:
    Runs the test with specified input CSV files.
    Runs test_keyword:
      Reads the input CSV file with test parameters.
      Applies the congestion control logic.
    Outputs test results to output.txt.

## Slide 24: Per-Flow Memory Use
Cubic + SEARCH (u32)
Cubic + SEARCH (u16)
Cubic + SEARCH (u8)
BBR
Cubic + HyStart
Cubic